## Slide 1
EKF-Based State Estimation and PID Offboard Control for PX4 UAV using ROS 2
Piyush Dubey
Aerial Robotics Kharagpur – Controls Team

## Slide 2
Project Goals
Achieving reliable autonomous flight necessitates precise state estimation and robust feedback control. While modern autopilots like PX4 offer optimized solutions, reimplementing these systems is vital for advanced research and development.
1
Custom EKF Design
Utilizing raw IMU and altitude measurements for enhanced state estimation.
2
Cascaded PID Implementation
Developing a robust controller for precise altitude regulation.
3
ROS 2 Offboard Interface
Interfacing with PX4 autopilot using ROS 2 for command and control.
All development and validation are performed in PX4 SITL using Gazebo and ros2 (Humble).

## Slide 3
Approach
01
EKF Design
Designed Extended Kalman Filter from first principles.
02
Sensor Fusion
Asynchronously fuse IMU and Altimeter data.
03
State Publication
Publish estimated state via ROS 2 topics.
04
Control Implementation
Cascaded PID for altitude control.
05
PX4 Interface
Interface with PX4 Offboard mode, adhering to safety protocols.

## Slide 4
High-Level System Architecture
System Architecture
ROS 2 EKF Node
Prediction and Measurement Update
ROS 2 PID Controller
Compute control setpoints
PX4 Offboard Interface
Send setpoints to vehicle
PX4 SITL Sensors
IMU and Altimeter data
Design Philosophy
Our system integrates custom ROS 2 nodes with the PX4 autopilot in a simulation environment, ensuring precise state estimation and robust control.
PX4 Remains Responsible for:
Angular rate control
Motor mixing
Safety and failsafes
External ROS 2 Nodes Provide:
State estimation (EKF)
High-level control commands (PID)
Attitude stabilization

## Slide 5
EKF-Based State Estimation
The Extended Kalman Filter (EKF) is crucial for accurately determining the UAV's orientation and vertical motion. It intelligently fuses various sensor data to provide a robust, real-time estimate of the drone's state.
1
State Vector Definition
Estimates roll (ϕ), pitch (θ), yaw rate (r), altitude (z), and vertical velocity (vz) to fully describe the UAV's critical dynamics.
2
Prediction Model
Uses IMU inputs (gyroscope and accelerometer) to propagate the estimated state and its uncertainty forward in time.
3
Measurement Updates
Integrates accelerometer data to correct roll and pitch, and altimeter data for altitude refinements.
4
Covariance Management
Continuously updates the state covariance matrix (P) and incorporates process noise (Q) for optimal estimation accuracy.

## Slide 6
Results
What Was Successfully Achieved
Stable EKF Execution
Achieved stable Extended Kalman Filter execution with accurately bounded covariance, ensuring robust state estimation.
Correct Sensor Fusion
Successfully fused IMU and altimeter data, providing a comprehensive and accurate understanding of the UAV's state.
Consistent Estimates
Generated physically consistent estimates for roll, pitch, altitude, and vertical velocity, critical for flight stability.
Functional PID Control
Implemented functional cascaded PID control logic, capable of precise altitude regulation in simulation.
Continuous Offboard Publication
Ensured continuous publication of PX4 Offboard heartbeat and setpoints, maintaining communication readiness.

## Slide 7
Current Status
Simulation Limitation Observed
During PX4 SITL testing, the vehicle did not successfully transition into full OFFBOARD control, remaining in nav_state = 14 (POSCTL). This prevented the execution of full autonomous flight.
This indicates unresolved PX4 Offboard mode constraints related to mode switching, command sequencing, or safety checks, despite the following components functioning correctly:
EKF Functionality
EKF estimation was functioning correctly, providing accurate state data.
PID Command Generation
PID control commands were generated as expected, ready for execution.
Offboard Messages
Offboard messages were published continuously and correctly.
Validation Scope
The work presented is therefore validated up to the following crucial stages:
01
Estimator Design & Implementation
The theoretical and practical aspects of the EKF estimator have been thoroughly validated.
02
Controller Logic & Safety Constraints
The PID controller's logic and adherence to safety protocols are confirmed.
03
ROS 2–PX4 Offboard Interface Structure
The communication architecture between ROS 2 and PX4 Offboard has been successfully established.
Full autonomous flight execution remains a key objective for future work.

## Slide 8
Key Learnings & Takeaways
Technical Learnings
EKF correctness hinges on robust covariance handling, not just state equations.
IMU-based estimation demands precise gravity modeling and consistent frame definitions.
Cascaded PID (position → velocity → thrust) provides superior stability over direct thrust control.
Mandatory safety limits (e.g., thrust saturation, heartbeat checks) are critical, even in simulation.
PX4 Offboard & System-Level Learnings
PX4 Offboard control relies on strict protocols and timing, not intuitive commands.
Mere publication of correct topics is insufficient for OFFBOARD activation.
Mode sequencing, arming logic, and heartbeat timing are vital for proper nav_state transitions.
PX4 can silently remain in POSCTL (nav_state = 14) if safety conditions are unmet.
Although full OFFBOARD flight was not achieved, this project gave us a deep, system-level understanding of why autonomous UAVs fail — which is more valuable than a single successful flight.